## Slide 1
Bayesian Modelling Workshop
3rd Session – Incorporating Prior Knowledge
April 13th, 2023

## Slide 2: Bayesian Modelling
: Model parameters
: Data
Posterior probability
(Not a point estimation)
Prior probability
(prior knowledge on )
Data likelihood

## Slide 3: Bayesian Linear Regression
Data Likelihood
Prior

## Slide 4: Bayesian Linear Regression
Bayesian with non-informative prior

## Slide 5: Bayesian Linear Regression with Positive Slope
Data Likelihood
Prior
Data Likelihood
Prior
Notes: 𝑝(𝜃_1 )≔𝐸𝑥𝑝(𝜃_1│𝜆=0.1)

## Slide 6: Bayesian Linear Regression with Positive Slope

## Slide 7: Bayesian Linear Regression with Positive Slope
Bayesian
With non-informative prior
Bayesian
with informative prior (positive slope)

## Slide 8: Bayesian Modelling
: Model parameters
: Data
Posterior probability
(Not a point estimation)
Prior probability
(prior knowledge on )
Data likelihood
Incorporate your knowledge and/or information from the literature
Deal with missing data/information  4th Session
Prior probability over functions!  5th Session

## Slide 9: Bayesian Material Property Calibration/Estimation
Create datasets from the FRP for empirical validation of simulation tools, which has limited input uncertainty compared to real buildings.
Provide modeling Input document + operational data
Demonstrate with a detailed EnergyPlus model

## Slide 10: Bayesian Material Property Calibration/Estimation
Temperature
Heat flux
Interior
Exterior
Gypsum
Batt Ins.
Concrete block
Air gap
Brick

## Slide 11
Internal node heat diffusion equation
discretization
Node temperatures
Boundary conditions
Process noise
Unconsidered factors influencing the dynamic
Model imperfection
Measurement noise
20 nodes (3 in gypsum, 6 in insulation, 10 in concrete block, 6 in face brick)
Bayesian Estimation with 1-D Finite Difference Heat Conduction Model

## Slide 12
Prior distributions for the other material properties (Gamma)
  mean: ~EP input values
  95% interval: ~30% of mean
Prior distribution for the density of the batt insulation layer (Gamma)
  Very flat hierarchical
~30% of mean
mean
Prior distribution for the density of the batt insulation layer (1/1000)
Bayesian Estimation with 1-D Finite Difference Heat Conduction Model

## Slide 13
R-value computed with median values = 3.625 [m2-K/W]
Air R
[m2-K/W]
Cp
[J/kg-K]
ρ
[kg/m3]
k
[W/m-K]
Gypsum
Batt
Gypsum
CMU
Face Brick
Bayesian Estimation with 1-D Finite Difference Heat Conduction Model

## Slide 14
1
2
3
1
2
3
Median values of the root of the diagonal components in the process noise covariance matrix: 0.00189 – 0.413
Median values of the root of the diagonal components in the Measurement noise covariance matrix: 0.408, 0.00712, 0.0124
Node temperatures
Boundary conditions
Process noise
Unconsidered factors influencing the dynamic
Model imperfection
Measurement noise
Bayesian Estimation with 1-D Finite Difference Heat Conduction Model

## Slide 15
Thank you!
(sjae.lee@utoronto.ca)
FAULT DETECTION AND DIAGNOSIS
ENERGY & DATA
MANAGEMENT
HUMAN-BUILDING INTERACTION
ENERGY SYSTEM
OPTIMAL CONTROL
GRID-INTERACTIVE CONTROL